## Slide 1: Industrial wood construction
Teaching materials for industrial wood construction education
2022

## Slide 2
Origin of the materials
These learning materials for industrial wood construction have been prepared in a project led by Puuinfo Oy in 2021–2022. Also involved in the project were
Lappia Vocational College,
TTS-Työtehoseura ry
South-Eastern Finland University of Applied Sciences,
Metropolia University of Applied Sciences,
Jyväskylä University of Applied Sciences,
University of Tampere, and
Federation of the Finnish Woodworking Industries Puutuoteteollisuus ry
The project was funded by the Ministry of the Environment.
The materials are intended to be used as extensively as possible in industrial wood construction education and studies.
The materials are released under the Creative Commons licence Attribution-ShareAlike (CC BY-SA), which requires that the author be properly credited when the materials are used and that derivative works may only be distributed under the same licence as the original work.
The original materials and any updates to them by Puuinfo will be published on the Library of Open Educational Resources website (aoe.fi) and the Puuinfo.fi website.
Use of the materials

## Slide 3: Construction physics

## Slide 4
Authors
Tero Lahtela, Insinööritoimisto Tero Lahtela Oy
Release date: 18/08/2021

## Slide 5: Acoustics

## Slide 6: Sound
Sound is a wave that travels through a medium.
The medium may be a gas, liquid or solid matter.
In air, sound travels as a longitudinal wave
In a solid matter, sound moves both as a traverse and longitudinal wave

## Slide 7: Airborne sound
Sound that travels through air is known as airborne sound
The human ear can detect airborne sound at frequencies of 20…20000 Hz
We also sense strong low-frequency vibration through our bodies
Airborne sounds are created inside and outside buildings

## Slide 8: Structure-borne sound
Sound moving through the frame of a building is known as structure-borne sound
Structure-borne sound generates airborne sound and vice versa
  Vibration in a building element generates vibration in the air surrounding this element and airborne sound
  When airborne sound comes into contact with a building element, it makes the element vibrate, creating structure-borne sound
A) Airborne sound at a building element
B) Impact caused by walking, etc.
C) Moving furniture, etc.
D) Supporting drains etc. to the frame
E) Appliances causing vibration
F) Vibration caused by traffic

## Slide 9: Sound propagation paths
In acoustic design, the building must always be examined as a whole
All sources of sound and its propagation paths must be accounted for
Only examining individual structural elements is not enough
Flanking transmission may significantly impair sound insulation between spaces
A) Through the building element
B) Through a flanking building element (flanking transmission)
C) Through air leaks in the building element
D) Through building services equipment (flanking transmission)
E) Through an open window (flanking transmission)

## Slide 10: Sound pressure [Pa]
Sound pressure p [Pa] is a change in air pressure compared to static pressure
The greater the change in air pressure, the louder the sound appears to our ears
The smallest air pressure change the human ear can hear as a sound is 0.00002 Pa (hearing zone)
The threshold of pain of the human ear is reached at an air pressure change of 20 Pa

## Slide 11: Sound pressure level [dB]
A logarithmic scale of decibels has been developed for indicating sound pressure levels Lp [dB], as indicating them as sound pressure p [Pa] is challenging
For instance, the ratio between the air pressures of the hearing zone and the threshold of pain is one to a million.
In practice, the logarithmic scale of decibels also makes it easier to perceive the sound pressure level
  As a numeric value, for example, 60 dB is a better indication of volume than 0.02 Pa

## Slide 12: Association between sound pressure and sound pressure level

## Slide 13: Impact of several sound sources

## Slide 14: Sound frequency [Hz]
Number of sound wave oscillations per second
The greater the frequency, the higher the sound appears to us
Phenomena dependent on audio frequency
  Sound pressure level produced by the source of sound
  Acoustic operation of a building element
  Sound insulation capacity of a building element

## Slide 15: Coincidence phenomenon
The vibration that a sound wavefront causes in a panel when it hits the panel surface at a certain angle has the same wavelength as the wavefront component parallel with the panel
The sound wavefront hitting the panel and the panel bending wave have the same phase, and the sound waves penetrate the panel

## Slide 16: Coincidence cut-off frequency fc
At coincidence cut-off frequency, the airborne sound insulation of a building element impairs significantly
Coincidence cut-off frequency is impacted by the panel’s
  Thickness
  Density
  Poisson’s ratio
  Modulus of elasticity
Cross-laminated timber panels (e.g. plywood, LVL, CLT) have different coincidence cut-off frequencies in different plane directions (bending stiffness)
The coincidence phenomenon is a particular challenge associated with wood panels

## Slide 17: Indicative coincidence cut-off frequencies

## Slide 18: Natural frequency f
The strongest vibration is created at the natural frequency of a material
Above the lowest natural frequency, other natural frequencies exist
Each natural frequency has its natural vibration form
The natural frequency depends on the following properties of the building element, structural component set or other similar system
  Mass
  Stiffness
  Dimensions

## Slide 19: Natural vibration forms of a building element

## Slide 20: Resonance
Resonance is generated when the frequency of an external stimulus corresponds to the natural frequency of a material
Sound insulation deteriorates in the resonance range but improves efficiently above it
The lowest natural frequency of a building element used for soundproofing must be as low as possible to ensure that the element insulates sound effectively in frequency range 100…3150 Hz

## Slide 21: Shear wave cut-off frequency fh
In addition to bending waves, shear waves occur in a panel
The shear wave curbs the increase in sound insulation capacity above the shear wave cut-off frequency
Significant in the case of thick panels at great frequencies
  Concrete structures
  Solid timber panel structures
Shear

## Slide 22: Airborne sound insulation
The purpose of airborne sound insulation is to reduce airborne sound travelling to the other side of a soundproofing building element
The airborne sound insulation capability of a building element is given as its sound reduction index Rw
Airborne sound insulation between spaces is given as standardized level difference DnT,w
  Flanking transmissions should be accounted for
  Surface area of the soundproofing building element
  Reverberation and size of the space
Airtightness of a building element is highly significant for airborne sound insulation
Flanking transmission is highly significant for airborne sound insulation

## Slide 23: Determination of airborne sound insulation

## Slide 24: Building element airtightness
Airtightness of a building element is a basic condition for airborne sound insulation, as sound travels through air
An air gap in a building element has some sound insulating effect but in practice, sound coming into contact with it can be expected to travel through the gap from one space to another

## Slide 25: Building element airtightness
Air leaks can be seen in the measurement graph at high frequencies

## Slide 26: Measuring airborne sound insulation
The airborne sound insulation of an individual building element can be tested with laboratory measurements
Field measurements can be conducted to examine building elements and the impacts of their joints and joining components on airborne sound insulation
A field measurement can be conducted
  In an actual building
  In a test building constructed with actual structures
As the sound source, an omnidirectional loudspeaker is usually used
The sound pressure level (90…100 dB) of the noise produced by the loudspeaker is roughly similar in each frequency band in the area 100…3150 Hz

## Slide 27: Measuring airborne sound insulation

## Slide 28: Airborne sound insulation measurement result
The standardized level difference DnT,w between spaces is calculated for each frequency band based on measured level differences DnT (measurement range 100…3150 Hz) using the reference curve method set out in standard ISO-717-1
The standardized level difference DnT,w is read in the reference curve at 500 Hz (the greater the numeric value, the better the airborne sound insulation)
The location on the reference curve is determined by moving it at 1 dB intervals, so that the sum of the curve values and the deviations of measured values below it is no more than 32 dB

## Slide 29: Airborne sound insulation measurement result

## Slide 30: Impact noise insulation
The purpose of impact noise insulation is to reduce the sound pressure level of impacts on the intermediate floor below the intermediate floor and in adjoining spaces
The impact noise insulation between spaces is given as the impact sound level index L’nT,w
  Flanking transmissions should be accounted for
The airtightness of a building element is highly significant for impact noise insulation
Flanking transmission is highly significant for impact noise insulation

## Slide 31: Determining impact noise insulation
Impact noise level L, which is usually detected in the space below, is examined using an impact noise machine placed on the intermediate floor
Rather than imitating walking on the intermediate floor, the impact noise machine produces continuous similar impacts on the intermediate floor, making it possible to measure the impact noise levels produced by them in another space

## Slide 32: Measuring impact noise insulation

## Slide 33: Impact noise insulation measurement result
The standardized level difference for impact noise LnT,w between spaces is calculated for each frequency band based on measured impact noise differences LnT (measurement range 50…3150 Hz) using the reference curve method set out in standard ISO-717-2
The standardized level difference for impact noise LnT,w is read in the reference curve at 500 Hz (the smaller the numeric value, the better the impact sound insulation)
The location on the reference curve is determined by moving it at 1 dB intervals, so that the sum of the curve values and the deviations of measured values above it is no more than 32 dB
Under regulations, spectral adaptation term Cl,50-2500, which accounts for frequencies below 100 Hz, must be included in the standardised level difference for impact noise

## Slide 34: Impact noise insulation measurement result

## Slide 35: Single-layer acoustics
Structures are considered to be single-layer when the same material is used throughout the structure or when different layers of materials are so closely bound together that they vibrate as a whole
Factors significant for designing airborne sound insulation are
  Mass
  Stiffness
  Airtightness
  Impact of flanking transmissions
In addition, flexibility of the surface structure (e.g. flooring) is also a significant factor in impact noise insulation design

## Slide 36: Acoustically simple structures

## Slide 37: Airborne sound insulation of a simple structure
The airborne sound insulation of an airtight simple structure is mainly based on mass and stiffness
According to the Mass Law, the airborne sound insulation of a structure increases by approx. 6 dB when
  The mass of the structure is doubled
  The sound frequency is doubled
Airborne sound insulation increases highly efficiently above the coincidence cut-off frequency up till the shear wave range

## Slide 38: Airborne sound insulation of a simple structure
A solid timber structure should be almost 600 mm in thickness to match the airborne sound insulation of a concrete structure 180 mm in thickness
Coincidence significantly impairs airborne sound insulation when the structure is light (also a concrete structure m < 300 kg/m2)

## Slide 39: Impact noise insulation of a simple structure
The impact noise insulation of an airtight simple structure is mainly based on mass and rigidity
A flexible flooring is highly significant for impact noise insulation
The impact noise levels produced by a simple concrete intermediate floor are low at low frequencies but increase with high frequencies

## Slide 40: Impact noise insulation of a simple structure
A flexible flooring or a floating surface plate is usually needed on top of a simple intermediate floor of concrete to reduce the impact noise levels at high frequencies
If the flooring is flexible, its impact noise reduction index ΔLw must be examined (not directly applicable to wooden intermediate floors)

## Slide 41: Dual-layer acoustics
A dual-layer structure has two plates (m1 and m2) with an air gap between them (k)
The air gap in dual-layer structures is called a spring, and its effectiveness as an insulator depends on the thickness of the air gap
The air gap acts as a spring when it is thicker than the wavelength of the sound applied to the structure
The looser the spring, the less it transmits vibration between the plates m1 and m2 (and the better the airborne sound insulation)
Rather than acting as a spring, a thin air gap connects the plates together, impairing the airborne sound insulation of the structure

## Slide 42: Ideal dual-layer structure

## Slide 43: Wood structures with dual-layer acoustics

## Slide 44: Dual-layer acoustics
Factors that are significant for designing the airborne sound insulation of a dual-layer structure are
  Weight of the plates, coincidence cut-off frequency and airtightness
  Resonance frequency of the mass-spring-mass system
  Mechanical connection between the plates
  Thickness of the air gap (rigidity of the spring)
  Impact of flanking transmissions

## Slide 45: Airborne noise insulation of a double wall
The airborne noise insulation of a double framed wall increases effectively above the resonance frequency up till the coincidence cut-off frequency
Coincidence impairs airborne sound insulation
When coincidence cut-off frequency is at the top end of the measurement range (3150 Hz), it has no significant negative impact on airborne sound insulation

## Slide 46: Airborne noise insulation of a double wall
The airborne noise insulation of a double framed wall with solid timber panel structure increases effectively above the resonance frequency up till the coincidence cut-off frequency
Coincidence impairs airborne sound insulation
When coincidence cut-off frequency is low, this significantly impairs airborne sound insulation

## Slide 47: Airborne noise insulation of a double wall
A plasterboard is often needed on a solid timber panel wall to meet the requirements set for a partition between flats
Plasterboard installed on a solid timber panel
  Improves airborne sound insulation at low frequencies
  Reduces the impact of coincidence on airborne sound insulation
Plasterboard can also be installed on the side of the air gap

## Slide 48: Impact of the thickness of solid timber

## Slide 49: Unsymmetrical wall structures

## Slide 50: Impact of guide pieces
Both frame halves should have their separate guide timbers
Adjacent guide timbers can be replaced with a single one that is the width of the gap in the wall if this is approved by the acoustics designer of the site
Coupling of frame halves with a guide timber impairs airborne noise insulation

## Slide 51: Impacts of connecting frame halves

## Slide 52: Impacts of connecting frame halves

## Slide 53: Impacts of connecting frame halves

## Slide 54: Impact of sound-absorbing material in a wall gap
Natural vibration of air (standing sound waves) is generated in the empty air gap of a double framed wall
In practice, the sound echoes in the empty air gap, which significantly impairs the airborne noise insulation of the wall
To prevent echoing in the air gap, it must contain sound-absorbing material (absorption ratio at high frequencies 0.8…0.9), covering at least one half of the air gap thickness

## Slide 55: Sound absorbing material in a wall gap

## Slide 56: Impacts of wall gap thickness
Increasing the thickness of the air gap in a double framed wall (k) significantly improves the airborne sound insulation of the wall
The thicker the air gap, the less it connects the plates of frame halves to each other

## Slide 57: Impacts of wall gap thickness
Dual-layer solid timber structures should have thin structural layers with large air gaps between them
Thick partitions between flats are today possible as only 200 mm of the walls are included in the permitted building volume
The solid timber product must be thick enough from the perspective of the structure’s load-bearing capacity

## Slide 58: Impact noise insulation of a dual-layer intermediate floor
Impact noise insulation is in a key role in the acoustic design of intermediate floors
The impact noise levels of wooden intermediate floors are high at low frequencies and low at high frequencies
Low frequencies are a challenge associated with wooden intermediate floors
In wooden intermediate floors, mass is required to insulate low frequencies

## Slide 59: Impacts of a spring suspension ceiling
A spring suspension ceiling significantly improves the airborne sound and impact noise insulation of a wooden intermediate floor
The positive impact on sound insulation generated by a spring suspension ceiling already begin at around 50 Hz
The more flexible and heavier the spring suspension ceiling is, the better the airborne sound and impact noise insulation

## Slide 60: Natural frequency of a floating floor
A floating floor acts as sound insulation at frequencies above its resonance range
The smaller the lowest natural frequency of a floating floor is, the better sound insulation is achieved
The dynamic rigidity of impact noise insulation and the mass of a floating floor influence the lowest natural frequency of a floating floor

## Slide 61: Impact of a floating floor

## Slide 62: Impact of flooring
The flooring does not have a significant impact on airborne sound insulation
In wooden intermediate floors, a flexible flooring affects impact noise insulation when the intermediate floor has a fixed surface floor
In case of a floating floor, the impact of flexible flooring on impact noise insulation has almost no significance

## Slide 63: Impact of intermediate floor frame
The impact of the rigidity and support types of the load-bearing frame of a wooden intermediate floor can be considered insignificant
The frame rigidity and support types of the wooden intermediate floor have a significant impact in intermediate floor vibration design (e.g. vibration caused by walking)

## Slide 64: Impact of a gap in intermediate floor
The same acoustic principles apply to an air gap in a dual-layer intermediate floor as to a dual-layer wall
The greater the air gap, the better the airborne sound and impact noise insulation
Echoing in the intermediate floor air gap is eliminated with a sound-absorbing material (min 100 mm)

## Slide 65: Suspended floors
Suspended floors are well suited for use together with solid timber panel intermediate floors
  It may be possible to use solid timber panel as the visible ceiling surface (surface quality)
The suspended floor and solid timber panel make up a dual-layer acoustic structure
The same acoustic principles mainly apply to intermediate floors with a suspended floor as to other wooden intermediate floors

## Slide 66: Intermediate floors of prefabricated box units
The ceiling of a lower prefabricated box unit and the floor of an upper one make up a dual-layer acoustic structure
The same acoustic principles apply to intermediate floors of prefabricated box units as to other wooden intermediate floors

## Slide 67: Structural flanking transmission
Structural flanking transmission is caused when a structural element that continues from one space to another propagates sound between the spaces (structure-borne sound)
In a building with wooden structure, structural flanking transmission is a greater challenge than in a concrete building because
  The mass and stiffness of building elements cannot be used to reduce flanking transmission in wooden structures
  The number of available wooden structure solutions is large, which is why design solutions must be selected case by case from the perspective of flanking transmissions
  The joints between wooden structures have more structural components, which is why even minor changes in these components may have a very significant impact on flanking transmissions

## Slide 68: Vibration insulators
Image: Getzner

## Slide 69: Vibration insulator in joints between CLT panels
Image: Getzner

## Slide 70: Vibration insulator in joints between CLT panels
Image: Getzner

## Slide 71: Structural flanking transmission

## Slide 72: Structural flanking transmission

## Slide 73: Structural flanking transmission

## Slide 74: Structural flanking transmission

## Slide 75: Structural flanking transmission

## Slide 76: Structural flanking transmission

## Slide 77: Structural flanking transmission

## Slide 78: Structural flanking transmission

## Slide 79: Structural flanking transmission

## Slide 80: Structural flanking transmission

## Slide 81: Structural flanking transmission

## Slide 82: Structural flanking transmission

## Slide 83: Structural flanking transmission

## Slide 84: Structural flanking transmission

## Slide 85: Structural flanking transmission

## Slide 86: Structural flanking transmission

## Slide 87: Structural flanking transmission

## Slide 88: Association between airborne sound insulation and speech

## Slide 89: Regulations
Apartment unit, Accommodation unit, Patient rooms of a residential institution

## Slide 90: Regulations
Apartment unit, Accommodation unit, Patient rooms of a residential institution

## Slide 91: Guidelines
Schools

## Slide 92: Guidelines
Day-care centres

## Slide 93: Guidelines
Offices

## Slide 94: Building services equipment
Building services equipment usually means equipment of the water supply and sewage systems as well as the ventilation, cooling and heating systems
Lifts, compressors, built-in vacuum systems and carpet vacuum cleaners as well as communal laundry room appliances (e.g. washing machine, spinner, tumble drier, mangle) are also regarded as building services equipment.
An air source heat pump is also a piece of building services equipment, and particular attention should be paid to the placement and vibration insulation of its external unit

## Slide 95: Concepts relating to building services equipment
LAeq,T refers to the equivalent continuous sound level of the equipment
LAFmax,T refers to the maximum sound level of the equipment when operating
EXAMPLE
  The equivalent continuous sound level is measured from the time a toilet is flushed until the sewage has left the pipe system and the noise is no longer audible
  The maximum sound level is the momentaneous peak sound level value during this measurement period

## Slide 96: Concepts relating to building services equipment
Continuous wide-frequency sound
  For example, the ‘humming’ of the ventilation system
Narrow-frequency sound
  For example, the ‘whistling’ of ventilation system terminal device
Impulse noise
  For example, the ‘clonk’ of the elevator mechanism when stopping
Wide-frequency sound is experienced as less disruptive than narrow-frequency and impulse noise
From health perspective, narrow-frequency and impulse noise are experienced as harmful

## Slide 97: Regulations
Building services equipment and lifts

## Slide 98: Guidelines
Building services equipment and lifts

## Slide 99: Methods for reducing noise from HVAC equipment

## Slide 100: Legend of HVAC equipment symbols

## Slide 101: Horizontal drains
Noise in drainage pipes is created by the substance flowing in the pipe
Sewers are usually placed in the intermediate floor
  They generate noise in the storey below, which is a space they do not serve
  The number of drains in intermediate floors should be minimised
The drain should be supported with heavy and rigid structural components
Leading the drain from the toilet seat directly to the HVAC conduit is advisable
Spaces that contain drains serving the same purpose should be centralised and placed side by side in the layout solution

## Slide 102: Supporting pipes with a rail system

## Slide 103: Horizontal drain sound insulation methods

## Slide 104: Horizontal drain sound insulation methods

## Slide 105: Horizontal drain sound insulation methods

## Slide 106: Horizontal drain sound insulation methods

## Slide 107: Horizontal drain sound insulation methods

## Slide 108: Horizontal drain sound insulation methods

## Slide 109: Horizontal drain sound insulation methods

## Slide 110: Horizontal drain sound insulation methods

## Slide 111: Horizontal drain sound insulation methods

## Slide 112: Horizontal drain sound insulation methods

## Slide 113: Horizontal drain sound insulation methods

## Slide 114: Horizontal drain sound insulation methods

## Slide 115: Horizontal drain sound insulation methods

## Slide 116: Horizontal drain sound insulation methods

## Slide 117: Horizontal drain sound insulation methods

## Slide 118: Vertical drains
Usually led through a HVAC conduit
The loudest noise is created when substance travelling in the drain hits the drain corner at the bottom
The angle of drain junctions should be 45° or less
The drain should be supported with heavy and rigid structural components
Fire technical issues are particularly important
  Conduit construction materials and surface classes
  Compartmentation properties of the conduit

## Slide 119: Sound insulation methods for vertical drains

## Slide 120: Sound insulation methods for vertical drains

## Slide 121: Sound insulation methods for vertical drains

## Slide 122: Sound insulation methods for vertical drains

## Slide 123: Domestic water and heat distribution system
The noise in water pipes is mainly caused by water flow in the pipe and sound propagated along the pipes
The faster the water flows in the pipe, the more noise the pipe generates
The pipe material has no impact on the loudness of the noise created by the pipe, but it can affect the way the sound is propagated along the pipe
Domestic water and heat pipes should be supported with heavy and rigid structural components
Plastic pipes inside sheathing are an advisable solution from the viewpoint of sound propagation

## Slide 124: Ventilation system
The sound produced in a ventilation system is mainly created by air flow in the ventilation channels
  The noise of the air flow is generated by the regulating and terminal devices in the channels as a consequence of changes in flow speed and pressure
When selecting the ventilation machine, attention should be paid to the following
  Noise level caused by fan motors
  Flexible connection method of channels to the machine to avoid structure-borne sound in the channel
  Vibration insulation of the mechanism

## Slide 125: Ventilation system
The floor of the ventilation machine room must be as heavy and rigid as possible
  No floating floors
When selecting the ventilation machine, attention should be paid to the following
  Noise level caused by fan motors
  Flexible connection method of channels to the machine to avoid structure-borne sound in the channel
  Vibration insulation of the mechanism

## Slide 126: Example of supporting a ventilation machine

## Slide 127: Penetrations
The penetrations for pipes, channels, cables, power sockets etc. in sound insulating and fire compartmentalising building elements must be sealed
Even a minor air leak in a penetration undermines significantly the sound insulation of the building element
By space specific building services solutions, penetrations can be reduced significantly

## Slide 128: Lift shaft
The noise of a lift is caused by the lift mechanism and movements of its equipment
The wall of a wooden lift shaft must be a dual-layer acoustic structure
A wooden lift shaft must be separated from the frame of the building

## Slide 129: Lift shaft

## Slide 130: Exit passageways
Exit passageways refer to stairwells and balcony access
Stairways and landings must be separated from flat frame structures to prevent harmful levels of structure-borne sound travelling into the flat
The following acoustic requirements must be met in a building that contains flats, accommodation units or patient rooms
  Wall between an exit and a flat DnT,w ≥ 39 dB when there is a door in the wall
  Wall between an exit and a flat DnT,w ≥ 55 dB when there is no door in the wall
  Landings L’nT,w + CI,50-2500 ≤ 63 dB in the horizontal direction from the exit passageway to the flat
  Stairwell reverberation time T ≤ 1.3 seconds

## Slide 131: Stairwell and balcony access

## Slide 132: Sound insulation of external sheathing
External noise is caused by e.g.
  Road, rail and air traffic
  Activities in an industrial estate
  External units of refrigeration appliances (compressor)
Noise coming into contact with external sheathing may be
  Momentary (e.g. aircraft)
  Continuous (e.g. urban traffic)
From the viewpoint of housing health and comfort, the most harmful noise includes
  Continuous impulse noise
  Narrow-frequency sound
  Low-frequency noise

## Slide 133: Sound level difference between outdoors and indoors
The sound insulation requirement for external sheathing is given as standardised level difference ΔLA [dB]
  Difference between the noise level coming into contact with external sheathing and permitted indoor noise level
  E.g. daytime equivalent continuous sound level difference LAeq,u - LAeq,s (A weighted)
The external sheathing must insulated sound as a whole so that the standardised level difference requirement ΔLA in question is met in all spaces consistent with the main use of the building
The requirement for the standardised level difference of the external sheathing ΔLA is given
  Primarily in zoning regulations
  An indicative minimum value also in building regulations

## Slide 134: Requirement for standardised level difference (ΔLA)

## Slide 135: Determining the sound insulation of external sheathing
The sound insulation of external sheathing consists of the sound insulation of the exterior walls, windows, doors and roof
The sound insulation achieved through this whole is affected by
  Sound insulation of the building elements
  Relative shares of building elements (e.g. impaired by a large surface area of windows)
In the standardised level difference index of the external sheathing, spectrum adjustment terms are used to account for the difference in nature between traffic noise and speech
  In connection with rail and air traffic noise Rw + C
  In connection with road traffic noise Rw + Ctr

## Slide 136: Determining the sound insulation of external sheathing
Airborne noise insulation indexes are determined for exterior wall building elements (wall, window, door) using e.g. the design method set out in Ympäristöopas no 108
Design methods that are more accurate than those in Ympäristöopas 108 are today available that make it possible to optimise the sound insulation of external sheathing building elements, achieving more cost-effective solutions

## Slide 137: Acoustic operation of an external wall

## Slide 138: Acoustic operation of an external wall

## Slide 139: Impact of window properties

## Slide 140: Impact of window properties

## Slide 141: Indicative airborne sound insulation figures

## Slide 142: Roof sound insulation
Roof sound insulation does not usually affect the sound insulation in connection with road and rail traffic noise
If noise from air traffic must be accounted for, the roof is usually designed to have 5 dB better sound insulation than the wall structure
Supply air noise sound suppressor is usually provided for in eaves
  Not needed in all cases (determined by acoustic designer)

## Slide 143: Acoustic operation of the roof

## Slide 144: Acoustic operation of the roof

## Slide 145: Room acoustics
Room acoustics is an important design area that requires special expertise
Echoing in a space, for example, significantly impairs speech clarity and also makes the space acoustically unpleasant in other respects
Depending on the purpose of the space, acoustics can be adjusted e.g. in the following ways
  In a space intended for making speeches, reflective surfaces are used to direct sound, and absorbing surfaces to improve speech clarity
  In spaces intended for relaxing and having conversations, absorption is used to shorten the reverberation time, which improves speech clarity and gives the space a calm feel in general
  In an open-plan office, the reflection of sound between workstations is reduced with powerful attenuation at the workstations

## Slide 146: Attenuation of a space
The larger the surface area of sound-absorbing material in a space, the more the sound power transmitted into or created in the space is reduced
Increasing the sound absorption in the space improves its soundscape but not sound insulation between the building elements connecting the spaces
Excessive sound absorption should be avoided
  Excessive sound absorption hampers e.g. conversation (speech is not carried)
  In high-absorption spaces, people must use a higher sound pressure level to be heard (increases the sound power coming into contact with sound insulating building elements)

## Slide 147: Absorption materials
Porous fibre-based products are normally used
  Mineral wool
  Cotton fibre wool
  Polyester wool
  Textiles
  Melamine foam
Sound energy causes the fibrous structure of the product to move, resulting in energy dissipation
When selecting products, attention should be paid to their fire technical properties (surface class)

## Slide 148: Sound absorption ratio
Absorption ratio α indicates the ratio between the sound intensity absorbed and coming into contact with the product
A product with α = 0 does not absorb the sound intensity that comes into contact with it at all
A product with α = 1 absorbs all sound intensity that comes into contact with it
The sound absorption ratio varies by sound frequency

## Slide 149: Sound absorption ratio
The absorption ratio is also affected by the product's
  Thickness
  Density
  Coating
  Installation technique
In practice, sound absorption products can be used to effectively attenuate high frequencies (short wavelength)

## Slide 150: Reverberation time
Reverberation time refers to the time during which the sound pressure level produced by a sound source is reduced by 60 dB, counted from the time when the source stops operating
In buildings with wooden structure, the wall and ceiling surfaces are mainly constructed with panels, which in themselves absorb some of the sound at low frequencies

## Slide 151: Reverberation time

## Slide 152: Speech transmission index
Speech transmission index (STI) is a numeric value that indicates speech transmission in a space
  STI = 1: all words can be heard clearly and correctly
  STI = 0: words cannot be made out at all
The STI value also indicates how well speech transmission between a speaker and a listener can be prevented
In some spaces, an excessively high STI value is a disadvantage
  E.g. workstations in an open-plan office

## Slide 153: Speech transmission index
The speech transmission index describes the comprehensive acoustic properties of a space, and it is affected by
  Reverberation time of the space
  Sound reflection in the space
  Background noise level in the space
  Shape of the space
  Location of absorption materials in the space
  Sound level of speech
  Distance between speaker and listener
  Properties and adjustments of sound reproduction equipment

## Slide 154: Speech transmission index

## Slide 155: Regulations and guidelines

## Slide 156: Repairs and alterations
As the starting point for acoustic requirements is regarded the regulations that were valid when the building was first completed
However, the acoustic properties may be better than the level set out in the regulations valid at the time of the building's completion
The acoustic properties and sound conditions of a building can never be impaired
An acoustic survey is carried out on a building to be repaired/altered to determine its current acoustic properties and sound conditions

## Slide 157: Repairs and alterations
When carrying out significant alterations, the acoustic requirements are examined on a case-by-case basis in connection with the building permit
The following are examples of significant alterations
  Alteration of flooring
  Alteration of floor surface structure
  Alteration of ceiling structure
  Alteration of sewer locations
  Alteration of water pipe locations
  Alteration relevant to ventilation
  Alteration of the locations of spaces on a storey
  Retro-fitting of a lift in a building

## Slide 158: Repairs and alterations
In connection with facade repairs, it may be necessary to remove the exterior shell of a sandwich element
If the interior shell is thinner than 150 mm, the flanking transmission caused by it must be reduced, e.g. using plates installed on spring elements

## Slide 159: Repairs and alterations
When building an additional storey, the old concrete roof pad of the building becomes an intermediate floor structure
The recommendation is that the intermediate floor between the highest storey with concrete structure and the additional storey is designed to have better sound insulation than required
New
New
The suspended floor must be dimensioned for vibration
Installation space for building services

## Slide 160: Repairs and alterations
Sound insulation of partitions may need to be improved, e.g. in a case where the purposes of use of spaces in a building are altered
A mass-spring-mass system can be improved using plates and/or an ‘air spring’
Sound insulation of an old building element can be improved with a mass-spring-mass system

## Slide 161: Repairs and alterations
Sound insulation must be examined as a whole, also accounting for the impact of possible structural flanking transmissions
In some cases, acoustic improvements are also needed in the floor and ceiling of a space due to structure flanking transmissions
Flanking transmission

## Slide 171: Example of a suspended floor
Image: Lindner
Image: Lindner